1. & 2.	Sets number of shots per game. Switch 1 sets tens, and                  		switch 2 sets units.

Example:- For 25 shots set switch 1 to read 2 and switch 2 to          		read 5.

3. 		Gun noise eprom.

4.		Gun noise volume control.

5.		Speed and pitch of gun noise (factory set).

6.		Piggyback board for electronic coin mechanism.

7.		Used only if ticket dispensers are fitted. Sets number of               		hits needed for one ticket.

8.		Output to score display.

9.		Output to shots left display.

10.		Factory set do not alter.

11.		Main board fuse 2 amp.

sheet 4