Shooting gallery Maintenance

Daily check

1. Drain compressor at the end of every day.

2. Check all guns and coin mechanisms are working.

3. Check all targets are working and are shooting water.

4. Check water level in tank.

5. At the end of the day switch the compressor off using the switch on top off the compressor, before switching the main supply to the gallery off.

Weekly Check

1. Check the oil level in the compressor

2. Before adding oil, turn off the compressor and drain the air from the tank.

Phone 0161 624 5578

Fax    0161 627 5357

Email info @pan amusements.com.

Technical sheets can be downloaded from our website

www.panamusements.com

Sheet 7