# Water system faults

No water squirters working

Is the water pump running ?

Yes								        No

Air in water system.				                  Is the water level low ?

Remove hexagon plug from

brass pump head and drain

some water out.				Yes					No

Add water			Is the float switch in

To tank      			the water tank 													operating ?

Yes				No

Clear obstruction

Is the pump relay

(next to the water pump)											operated ?

Yes						No

Change pump			      	check voltage and

wiring at the relay